## Slide 1: DICOM Educational Conference Chennai, India
October 9-11, 2023

## Slide 3: DICOM : A Family of Protocols
Protocol
  Specifies how two systems exchange information
Many kinds of Systems:
    Modalities, PACS / VNA, RIS, Workstations, EMR, …
Many kinds of Information:
    Images, worklists, measurements, surfaces, audit logs, …
…
Notes: First thing to understand: DICOM is how Systems talk to each other about imaging
Might think of DICOM as a file format, more accurate to say…
Many protocols in the family – related but independent

## Slide 4: Routine Clinical Practice of Imaging
Medical Imaging
Scheduling Imaging Procedures
Acquiring Images
Managing Images
Processing Images
Displaying Images
Reporting Images
Distributing Images
Notes: The bulk of the things we’ll look at are attempts to address PRAGMATIC needs of routine radiology/cardiology practice; rather than, research, etc. Usable for other purposes but DESIGNED for clinical practice.

## Slide 5: Store Images
DICOM stores your images
All kinds of images
CT, MR, X-Ray, Ultrasound, Angio, PET, Pathology, Ophthalmology, Medical Photography, Scanned Docs, …
Single & Multiframe; Volumes & Cines; B&W & Color; Original & Processed
DICOM manages your images
Not just pixels; Significant meta-data (“header”)
Patient ID & demographics, the order, equipment, acquisition, workflow, …
PACS/VNA = database; DICOM = machine readable
Can query / sort / autoroute / manage
Notes: What do the pixels mean? Real-world size, patient positioning, imaging technique, staining, …
Management is not easy. Consider how many images there are…
Places like the Mayo Clinic and Cleveland Clinic have 6+ billion DICOM images. Any large hospital is likely creating millions per year.

## Slide 6: Other DICOM Functions
Store (Imaging) Data
  Fetal growth, cardiac output, tumor size, CAD findings, ECG waveforms
Manage (Imaging) Workflow
  Modality worklists, progress updates, Storage Commitment
  Display Images
  Screen calibration, annotations, hanging protocols, key image flagging
Notes: TODO – update middle thumbnail for worklist

## Slide 7: Other DICOM Functions
Distribute Images
  Network push/pull, Media Transfer (CD, USB, DVD…), Email Attachments, Web Protocols (DICOMweb)
  Store Analysis Results
  Registrations, Segmentations, 3D Print Models, Bulk Pathology Annotations, …
  Security
  Audit Trails, De-identification Schemas, Encryption, TLS, …

## Slide 8: DICOM is not Static
DICOM first published in 1993.
Extended regularly to meet the expanding needs of Medical Imaging:
  Multi-energy CT
  3D Ultrasound
  Web-based PACS
  Whole Slide Imaging
  Clinical Measurements
  Radiation Dose Reporting
  Image Registration & Segmentation
  Computer Aided Detection / Diagnosis
  and Many, Many More . . .
Notes: DICOM has been evolving for almost 30 years because medical imaging has been evolving; new modalities continue to emerge.

## Slide 9: DICOM Change Process
Supplements for major changes
  New object types, new services, new compression schemes
  About 10 / year
  Developed by Working Groups
  Require Work Item approved by DICOM Standards Committee
Change Proposals for minor corrections
  About 100 / year
  Anybody can submit
  Backward Compatibility: Avoid changes that break existing implementations
Continuous maintenance process
  WG-06 (“Architecture Review Board”) meets five times per year
  All documents published for open Public Comment; later formal vote by Letter Ballot
Notes: There are two major mechanisms for updating DICOM - Supplements and Change Proposals. Supplements are used for major increments of functionality within the Standard, such as new types of image objects, new services, or new compression schemes. Change Proposals are used for clarification of the text of the Standard, or minor additions to existing functionality, such as new optional data elements within an image object definition.
A Supplement requires a formal Work Item approved by the DICOM Standards Committee. The Work Item assures that the scope of the proposed change is consistent with the strategic direction of DICOM, and the task is assigned to one of the DICOM Working Groups
A Change Proposal may be submitted by any user of the DICOM Standard at any time. All CPs are carefully reviewed to assure backward compatibility.
Changes are officially valid as soon as the final text of the supplement or CP is approved. A revised edition of the Standard with all the changes is published free on the DICOM web site. However, it is the responsibility of equipment vendors to keep up with the standard.

## Slide 10: Some Recent Supplements
Sup 202 Real Time Video
Sup 203 DICOMweb: Thumbnail Service
Sup 221 Dermoscopy
Sup 208 OBJ Encapsulation for 3D Manufacturing & VR
Sup 220 MR Prostate Imaging SR
Notes: 222: Microscopy Bulk Simple Annotations Storage (2021)
217 Neurophysiology Waveforms, 212 XA Protocol Storage,
Note WIP on Confocal Microscopy both in vivo and in vitro for dermatology applications

## Slide 11: DICOM Working Groups
Modality, clinical domain, or technology expertise:
Assigned to develop Supplements or Change Proposals
WG-01: Cardiac and Vascular Information | WG-18: Clinical Trials and Education
WG-02: Projection Radiography/Angiography | WG-19: Dermatology
WG-03: Nuclear Medicine | WG-20: Integration of Imaging and Info Systems
WG-04: Compression | WG-21: Computed Tomography
WG-05: Exchange Media | WG-22: Dentistry
WG-06: Base Standard | WG-23: AI & Application Hosting
WG-07: Radiotherapy | WG-24: Surgery
WG-08: Structured Reporting | WG-25: Veterinary Medicine
WG-09: Ophthalmology | WG-26: Pathology
WG-10: Strategic Advisory | WG-27: Web Technology for DICOM
WG-11: Display Function Standard | WG-28: Physics
WG-12: Ultrasound | WG-29: Education, Communication & Outreach
WG-13: Visible Light | WG-30: Small Animal Imaging
WG-14: Security | WG-31: Conformance
WG-15: Digital Mammography and CAD | WG-32: Neurophysiology
WG-16: Magnetic Resonance | WG-33: Data Archiving & Management
WG-17: 3D Printing | WG-34: Photoacoustic Imaging
Notes: Working Groups can be established to develop the standard for a particular modality, for a particular clinical domain, or for a particular functional capability.
Working Group 6, the Base Standard working group, is the architecture review board – it is responsible for ensuring the coherence, clarity, and quality of the DICOM Standard. All changes are reviewed several times by Working Group 6

## Slide 12: Maintaining Stability
No “Versioning”
  It’s just “DICOM” Not “DICOM 3.1”, “3.2”, “2021b”, etc.
Notes: The SOP Class-based Compliance Model- how DICOM has expanded its capabilities over 20 years while maintaining backward compatibility"

## Slide 13: DICOM SOP Class
Service + Object = Service Object Pair (Storage + MR Image = MR Image Storage)
SCU
SCP
MR Image Storage SOP Class
SCU – Service Class User
the system that uses the service (client)
SCP – Service Class Provider
the system that provides the service (server)
Notes: A bit of jargon terms that might come up in subsequent presentations or encounters with DICOM – you’re now a DICOM geek.
SOP Classes are key to DICOM. They form the context for any given communication so both sides know the rules.
Compliance is by SOP Class. If we need new rules, it’s easy to do inside a new SOP Class.

## Slide 14: Maintaining Stability
No “Versioning”
  It’s just “DICOM” Not “DICOM 3.1”, “3.2”, “2015b”, etc.
DICOM evolves by adding new “SOP Classes”
  New SOP Classes are added
  Old SOP Classes don’t “break”
  Most applications continue to support older SOP Classes when supporting new ones
Notes: Unlike other standards, such as HL7, DICOM evolves by adding extensions, not by creating a new version of an existing capability. Those capabilities – to which an implementation claims conformance – are “SOP Classes”. Once a SOP Class is defined, any changes to it are minor, and are fully forward- and backward-compatible.
With the Supplement process new features can be added to DICOM, but these are typically new SOP Classes, and they do not replace existing capabilities, they add new capabilities to which a product can claim conformance.
So a product can support multiple capabilities at the same time. And DICOM products determine exactly how they can interoperate every time the establish a connection, by negotiating the SOP Classes that they support.
And every DICOM conformant product comes with a Conformance Statement, so that humans can also see whether two systems will interoperate – which capabilities (that is, SOP Classes) it supports, and how the system uses those capabilities.

## Slide 15: DICOM Conformance
AKA “Getting the DICOM stuff you need, and hooking it up so it works”
SOP Classes are the basis of conformance and compatibility
Products conform to SOP Classes – not to a version of the Standard
DICOM publishes new editions regularly (e.g. 2023d)
  SOP Classes are added, but not changed incompatibly
Each SOP Class is stable
  forward and backward compatible across editions
  any new data elements are optional
Products conforming to the same SOP Class interoperate
  Humans compare DICOM Conformance Statements (DCS)
  Machines do Association Negotiation
Notes: The SOP Class-based Compliance Model- how DICOM has expanded its capabilities over 20 years while maintaining backward compatibility"

## Slide 16: Documented Assertion of Conformance
DICOM Conformance Statement
  Required for every compliant product – (see DICOM Part 2)
  Published on vendor websites
  Lists the SOP Classes & roles supported by a product
  Allows user organizations (or system integrators) to check compatibility
  Also describes product implementation details and behaviors (handy information for configuration and troubleshooting)
Notes: This product supports this list of SOP Classes; here are some details about how the SOP Classes have been implemented and how the system behaves when it uses them”

## Slide 17: Machine Negotiation of Capabilities
Before two systems perform a DICOM transaction they first agree:
  what SOP Class they will use (e.g. MR Image Storage)
  who will be the SCU (client role), who will be the SCP (server role)
  what compression will be used (e.g. JPEG Lossless)
This process is called Association Negotiation (“Handshake”)
AE_TITLE1
MR Image Storage
AE_TITLE2
<Request>
<Response>
Notes: Association Negotiation
Software can determine if two systems are compatible
Happens each time two DICOM systems open an association (connection)
They negotiate which SOP Classes will be used, and how (e.g. Transfer Syntax)
Based on what each system supports and/or prefers

## Slide 18: IHE in One Slide
IHE helps vendors implement & test functions that span multiple systems
Profiles are implementation guides
  how to use existing standards
  to address a specific problem scenario
Connectathons are test events
  managed testing of Profile implementations
IHE helps users purchase & integrate multi-system solutions
  list required IHE Profile support in RFPs
Notes: Connectathon: one week, 100+ vendors, 550+ engineers, thousands of tests. Non-trivial engineering event.

## Slide 19: IHE in One Slide
IHE helps vendors implement & test functions that span multiple systems
Profiles are implementation guides
  how to use existing standards
  to address a specific problem scenario
Connectathons are test events
  managed testing of Profile implementations
IHE helps users purchase & integrate multi-system solutions
  list required IHE Profile support in RFPs
Notes: Connectathon: one week, 100+ vendors, 550+ engineers, thousands of tests. Non-trivial engineering event.

## Slide 20: IHE Radiology Profiles
Examples to consider (all make use of DICOM): profiles.ihe.net
IHE SWF.b – Scheduled Workflow
IHE REM – Radiation Exposure Monitoring
IHE XDS-I – Cross-Enterprise Document Sharing for Imaging
IHE IDEP – Import and Display of External Priors
IHE EBIW – Encounter-Based Imaging Workflow
IHE AIR – AI Results
IHE AIW-I – AI Workflow for Imaging
IHE AI in Imaging Whitepaper

## Slide 21: Encounter-based imaging with DICOMweb
Image Manager/ Archive
Encounter Manager
Get Imaging Context
Store Images
https://encountermanager.here.org/workitems?AdmissionID=987654
&ScheduledProcedureStepSequence.ScheduledStationAETitle=DermTab1
[ {
“PatientName”: {"vr": "PN", "Value": [{"Alphabetic": "SMITH^JOHN"}]},
“PatientID”: {"vr": "LO", "Value": ["66437748"]},
“IssuerOfPatientID”: {"vr": "LO", "Value": [“Metrocity General Hospital"]},
“PatientBirthDate”: {"vr": "DT", "Value": ["19670701"]},
“PatientSex”: {"vr": "CS", "Value": ["M"]},
“InstitutionName”: {"vr": "LO", "Value": ["Metrocity General Hospital"]},
“InstitutionalDepartmentName”: {"vr": “LO", "Value": [“Dermatology"]},
…
https://mypacs.here.org/studies
Content-Type: application/dicom+json
[ {
“PatientName”: {"vr": "PN", "Value": [{"Alphabetic": "SMITH^JOHN"}]},
“PatientID”: {"vr": "LO", "Value": ["66437748"]},
“IssuerOfPatientID”: {"vr": "LO", "Value": ["Metrocity General Hospital"]},
“PatientBirthDate”: {"vr": "DT", "Value": ["19670701"]},
…
“BodyPartExamined”: {"vr": "CS", "Value": [“CALF"]},
“Laterality”: {"vr": "CS", "Value": [“R"]},
…
Content-Type: image/jpeg
<the image>

## Slide 22: Example: Using FHIR and DICOMweb for AI Training
Patient | Date
2345 | Jan. 17, 2014
4567 | Mar. 23, 2015
Tell me all patients who have had pneumonia.
GET https://ehr.hospital/fhir/Condition?code=233604007
Give me the images for that Chest study.
GET https://pacs.hospital/studies/?PatientId=2345
Study | Type
1.2.3 | X-Ray Chest
1.2.6 | CT Head
GET https://pacs.hospital/studies/1.2.3
Tell me all studies for each patient.
*Slide: Brad Genereaux
Notes: Photo by CDC on Unsplash

## Slide 23: DICOM SR (“Structured Reporting”)
SCCORD: Path = POLYLINE (32,77),(210,93)
NUM: Distance = 37.6 mm
INFERRED FROM
SELECTED FROM
IMAGE: 1.2.840.276453….
*Slide: David Clunie

## Slide 24
CONTAINER: "Individual Impression/ Recommendation"
CONTAINS
CODE: "Single Image Finding" = "Mammography breast density"
HAS PROPERTIES
SCOORD: "Outline" = POLYLINE {2531,2114,2537,2114,.. ,2531,2114}
SELECTED FROM
IMAGE: 1.2.840.276453….
SCOORD: "Center" = POINT {2505,2168}
CONTAINER: “Mammo CAD Report”
CODE: “Summary” = “Succeeded with Findings”
…
*Adapted from Slide: David Clunie
…

## Slide 25: DICOM SR Templates
Many Templates in Part 16:
Echocardiography Procedure Report
Mammography CAD
Radiation Dose SR (RDSR)
OB/GYN US Procedure Report
Colon CAD
CT/MR Cardiovascular Analysis
Cardiac Cath Report
…

## Slide 26: DICOM Sup219 – Simplified SR in JSON
Result File “Business Names”

## Slide 27: DICOM GSPS & KOS
Greyscale Presentation State Key Object Selection
Area Of
Interest
Notes: Now that film is gone and IT doesn’t like you putting grease pencil marks or post-it notes on the monitors,…

## Slide 28: DICOM Information Model (Query)
Instances - holds acquired data (Images or other IODs)
Series - groups related Images (same step/protocol/device)
Study - groups all Series for a given Requested Procedure
Patient - groups all Studies for that patient
DICOM uses Unique Identifiers (UIDs) to identify:
  specific Instances (“objects”)
  specific SOP Classes
  specific Study / Series
  . . . and many other things
Patient
Study
Series
Instance
(Image)
1..n
1..n
1..n
Notes: The information model represents the data created and managed in DICOM.
Note multiple series may be created for a single PPS, protocol, equipment
Note UIDs are intended for machines to read, not humans (UIDs long strings of numbers that are inconvenient for humans)

## Slide 29: Starting from the bottom ...
Storage Service
Service Class User
Service Class Provider
MR Storage SOP Class
MR Object
Module
Module
Module
+
Attribute
Attribute
Attribute
Notes: When you read you begin with A-B-C
With DICOM you begin with two AE’s
… Hmmmm
Let’s see if we can make it a bit easier:
Att-ribute to hold the stuff
Tag – to flag it with a code
VR – the kind of stuff it is
VM – how many things it holds
Macro – a way to copy tags
Module – looks just like a macro
IOD – the object that it makes
And a Service makes it go (go, go, go)
…
Tag, SOP, SOP, UCUM Code, Service Class, parent node…

## Slide 30: DICOM Terms: Attribute
Tag | Attribute Name | VR | VM | Value
(0010,0010) | Patient Name | PN | 1 | Smith^John^^^
Tag (Group #, Element #): to identify an attribute/data element
Value Representation (VR): data type used to encode the value(s)
Value Multiplicity (VM): how many values can be in the attribute
DICOM Data Stream = …00100010Smith^John^^^…
(See DICOM Part 6: Data Dictionary)
Notes: 0010,0020 Patient ID
CS, FL, DT
Parts 5, 7, & 8 get into the byte details of how exactly the datastream is encoded. Mostly handled by toolkits/libraries.

## Slide 31: DICOM Terms: Module
Attribute | Tag | Type | Attribute Description
Patient Name | (0010,0010) | 2 | Patient’s Full Name
Patient ID | (0010,0020) | 2 | Primary hospital identification number or code for the patient
Issuer of Patient ID | (0010,0021) | 3 | Identifier of the Assigning Authority that issued the Patient ID
… |  |  | 
Module: an architectural convenience; a logical group of attributes about a common topic
Macro: purely an editing convenience; a table of attributes that can be easily copied into modules
Type: (1) Required (2) May Be Empty if Unknown (3) Optional (1C or 2C) Conditional
Patient Module
(See DICOM Part 3: Information Object Definitions)

## Slide 32: DICOM Terms: Object (IOD)
Information Entity (IE): a group of modules representing a Real-World object
Reference: a Section in Part 3 where it is defined
Usage: (M) Mandatory; (C) Conditional; (U) Optional
IE | Module | Reference | Usage
Patient | Patient | C.7.1.1 | M
… |  |  | 
Equipment | General Equipment | C.7.5.1 | M
Image | General Image | C.7.6.1 | M
 | Contrast/Bolus | C.7.6.4 | C – Required if contrast media was used in this image
 | CT Image | C.8.2.1 | M
Enhanced CT Object
(See DICOM Part 3: Information Object Definitions)

## Slide 33: Optional & Private “Tags”
Optional Attributes (Type 3)
Type 3 does not mean “not useful”
  Several reasons for attributes to be Type 3
Optional doesn’t mean users can’t ask/insist on it
  If you need it in your practice, talk to your vendor
Private Attributes
Often device-specific details or custom functions
Ask your vendor for documentation (check DCS)
  Private Data Element​ Characteristics Sequence (0008,0300) can (optionally) provide inline documentation

## Slide 34: The DICOM Standard
Administered and Published by:
  NEMA (National Electrical Manufacturers Association) and it’s medical imaging division:
  MITA (Medical Imaging Technology Alliance)
Intellectual Property
  DICOM Trademark and Copyright is held by NEMA
  No license required to use the DICOM Standard in products
dicomstandard.org
  Download free electronic copies of all 22 Parts of the Standard
  Plans and activities are publicly posted
  ISO publishes Part 1 of the Standard as ISO 12052

## Slide 35: XML / Web publication
http://dicomstandard.org/current
DICOM Standard is free, in multiple formats:
  PDF - for fast searching
  XML - for automatic update of tools
  HTML - for easy use with hyperlinks to references
  MS Word - for extraction into project documentation
Re-published several times per year to incorporate all approved Supplements and Change Proposals

## Slide 36
Thanks for your attention!
Questions ?

## Slide 37: DICOM Whole Slide Microscopy Image
Key Features:
  Tiled Pyramid of Frames (multiresolution)
  Details for specimen identification, preparation, illumination, filters
  Handles localizers, labels, navigation, spatial coordinates
  (Recently) Bulk Annotations (Sup 222)
Significant implementation over last 5yrs; Viewers implementing DICOMweb
https://dicom.nema.org/medical/dicom/current/output/chtml/part03/sect_A.32.8.3.html
Notes: Sup 145 Whole Slide Imaging in Pathology 2010.08
Moves toward Enterprise Imaging, particularly in large hospitals, has been looking to harness economies of scale and robustnss.
Vendors have been starting to implement DICOM, Connectathons have been held with scanners, archives and viewers.
Due to the fresh territory, lots of adoption of DICOMweb which is a more natural fit for cloud-based solution architectures.
This also makes it fortuitously ripe for AI tools

## Slide 38: DICOM : Traditional Data Standard
Define how to encode & exchange information with unambiguous semantics
Broad scope
  Intentionally addresses MANY use cases
  “Swiss Army Knife”
  Generalized, inclusive
Priority: make most/all things possible
  You decide how to apply it to your problem

## Slide 39: IHE : Profiling
Profiling: Describing the application of existing standards to address a specific use case
Narrower Scope:
  Focus on ONE use case
Constrain Underlying Standards
  Select among alternative methods
  Remove/reduce optionality
Priority: Interoperability; common usage