## Slide 1: JPEG XL
DICOM Supplement 232

## Slide 2: Benefits of JPEG XL
Significantly smaller images for WSI
  Lossy compression for WSI has been accepted by regulators using JPEG
  Safari and Firefox both support JPEG XL
Supports lossy >8 bit compression
Ability to forward migrate into JPEG XL without any loss of fidelity with existing JPEG, as a safe migration option with full backwards compatibility
As DICOMweb response is multiframe at much higher quality than gif
As lossless web response, is much smaller than PNG and easier to decode
Works well for both natural and synthetic images

## Slide 3: Issues with JPEG XL
Not yet supported in all browsers, mitigated by WASM javascript modules (still zero footprint)
Acknowledge potential effect of any lossy compression on CAD AI or quantitative algorithms.
Patent issue that had occurred with Microsoft was determined to not be relevant by the JPEG XL community

## Slide 4: Experience with WSI with JPEG XL
Limited testing with JPEG XL at Mayo (6 months overall, 3 months concerted)
No visual difference from what is seen, with 50-60% smaller
  Multiple tiles, not all in one file
Site has 40 million slides
Very interested in the lossless transcoding from JPEG to JPEG XL
Testing is not exhaustive yet
Both multi-resolution in a single file and separated files
Profiling results show that JPEG XL is fast enough for decoding/encoding, but is not as fast as JPEG

## Slide 5: Vendor Perspective
WSI scanner vendors are interested in trying to generate JPEG XL directly
Reduction in artifacts is important for algorithms processing, and is better with JPEG XL
Streaming of data to both algorithms and viewers is important and better with JPEG XL
Can render portions of a tile that are important first (progressive)
WSI has archives several times bigger than radiology
  Mayo ~ 4 petabytes of data per year
May well be able to reduce quality to reduce size further without reducing machine or user quality as JPEG XL has lots of options with very few artifacts
Working on multi-spectral and multiple z-depths already, which is not well supported, and adds another order of magnitude in storage size

## Slide 6: DICOMweb Usage
Need to add JPEG XL transfer syntaxes to DICOMweb
JPEG XL provides an alternative to gif for multiframe rendered
JPEG XL is a logical extension to baseline JPEG, especially if easily supported in browsers.
JPEG XL is useful for color/lossy images as a replacement for JPEG whereas the HTJ2K is not very good for lossy compression, and is very good at lossless compression