## Slide 1: Supplement 241: STRUCTURAL HEART PROCEDURAL SR TEMPLATE WG-01/WG-12 Public Comment
06 November 2024

## Slide 2: Overview
Scope:
Periprocedural imaging for Structural Heart procedures.
  Structural Heart procedures are trans-catheter techniques to repair or replace a valve and treat structural abnormalities of the heart.
  Periprocedural imaging includes pre-operative assessment, intraprocedural assessment, and follow-up for Structural Heart Procedures.
Intended for multimodality use: CT (or MRI), and echocardiogram.
Procedures include:
  TAVI: Transcatheter Aortic Valve implantation
  TAVR: Transcatheter Aortic Valve Replacement
  TTVP: Transcatheter Tricuspid Valve Procedure
  TTVR: Transcatheter Tricuspid Valve Repair
  TEER: Transcatheter Edge-to-Edge Repair
  TMVr: Transcatheter Mitral Leaflet Clip Procedure
  TMVR: Transcatheter Mitral Valve Replacement
  LAAC: Left Atrial Appendage Closure

## Slide 3: Background
Pre-operative assessment: CT and/or echocardiography are commonly used for detailed anatomical assessment of the heart, aiding in the planning of transcatheter approaches and proper sizing of implants.
Intraprocedural assessment: Echocardiography and fluoroscopy are utilized for continuous monitoring during the procedure, ensuring accurate device deployment, positioning, and function.
Follow-up evaluation: CT and/or echocardiography are commonly employed for assessing device placement, function, and identifying potential complications such as perivalvular leaks or device migration during post-procedural follow-up.
Standardized measurements have been established by implant manufacturers, the Society of Thoracic Surgeons (STS) and the American College of Cardiology (ACC) for all three periprocedural phases.

## Slide 4
Structural Heart Procedure Report
TID newTID1
Language of Content Item and Descendants
TID 1204
Observation Context
TID 1001
Cardiovascular Patient Characteristics
TID 3602
Pre-coordinated Cardiac Measurement
TID 5301
Post-coordinated Cardiac Measurement
TID 5302
Adhoc Measurement
TID 5303
Wall Motion Analysis
TID 5204
Medications and Mixture Medications
TID 8131
Medical Device Use
TID 3831
4
Copyright DICOM® 2024
2024-11-06
Design Choices
Used Existing SR SOP class (Comprehensive)
Renamed Simplified Echo Procedure sub templates, TIDs 5301, 5302 and 5303 to support multimodality image acquisition.
Defined pre-coordinated terms

## Slide 5: Terminology
Context Identifier | Context Group Name
newCID1 | Structural Heart Procedures
newCID2 | Structural Heart Devices
newCID3 | Structural Heart Measurement
newCID4 | Structural Heart Aortic Valve Measurement
newCID5 | Structural Heart Mitral Valve Measurement
newCID6 | Structural Heart Tricuspid Valve Measurement
newCID7 | Structural Heart Echo Measurements
newCID8 | Left Atrial Appendage Closure Measurement
newCID9 | Structural Heart Procedure Anatomic Site
newCID10 | Peripheral Access Anatomic Site
newCID11 | Indication for Structural Heart Procedure
newCID12 | Bradycardiac Agents
newCID13 | Transesophageal Echocardiography Scan Planes
Sources:
Peer review publications
STS/ACC registry data elements
ASE guidelines
Device Inserts (Watchman, Amulet, MitraClip)
IHE CPN (Cardiac Procedure Note)
Clinical Applications
Copyright DICOM® 2024
2024-11-06