## Slide 1: Supplement 227: Ultrasound Elastography SR
Working Group 1/12: Cardiology/Ultrasound
Public Comment – 2021 December

## Slide 2: Overview
Scope: Ultrasound shear wave elastography
  Open Issue: Address Strain Elastography?
  Closed Issue: MRE is out of scope
SR template is proposed for elastography of organs/tissues such as liver, breast, prostate

## Slide 3: Background
Ultrasound can measure the speed at which an induced shear wave propagates through tissue (Shear Wave Speed in m/s).
SWS depends on the stiffness of the tissue and thus can be converted into an estimated Elasticity in kPa.
A SWS elastography report typically involves drawing 3-12 ROIs (usually circles or squares) at differing depths on the acquired images, recording the mean and Standard Deviation values for SWS and Elasticity within each ROI, and then computing specific summary statistics across the ROIs.

## Slide 4: Design Choices
Use existing SR SOP Classes
- Follows the precedent of most other Ultrasound reports
Add a general Ultrasound Report root template
- All existing Ultrasound roots were very application specific
- Based on Vascular root (which several vendors already do)
Add an Ultrasound Elastography sub-Template

## Slide 5: Example Result Tables
ROI # | Shear Wave Speed (m/s) |  | Elasticity (kPa) |  | Dispersion (m/s/kHz) |  | ROI Depth (cm)
 | ROI Mean | ROI SD | ROI Mean | ROI SD | ROI Mean | ROI SD | 
1 |  |  |  |  |  |  | 
2 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
R |  |  |  |  |  |  | 
Summary Statistics | Shear Wave Speed (m/s) | Elasticity (kPa) | Dispersion (m/s/kHz)
Mean |  |  | 
SD |  |  | 
Median |  |  | 
IQR |  |  | 
IQR/Median |  |  |