## Slide 1: Supplement 226
Confocal microscopy
DICOM Working group-19 Dermatology
Public comment
Editor: Liam cafferY
October 2022

## Slide 2: Confocal microscopy
Non-invasive imaging technique
Can be done in-vivo or ex-vivo
Used for the diagnosis of range of skin disease with an emphasis on melanoma
Precise diagnosis in difficult lesions

## Slide 3: In-vivo confocal microscopy
Allows examination of the skin at resolutions comparable to histology without performing a biopsy
Virtual biopsy
Adjunct to dermoscopy (or clinical imaging) as provides cyto-architectural architecture of different dermoscopic pattern
Acquisition in reflectance mode

## Slide 4
Dermoscope
MICROSCOPE
MICROSCOPE

## Slide 5: In-vivo confocal microscopy acquisition
Window attached to skin
Dermoscopic image acquired
Confocal microscope placed in window
User interface: Acquisition area drawn on dermoscopic image
Stage co-ordinate are transmitted to confocal microscope (up to 8mm x 8mm)

## Slide 6: In-vivo confocal microscopy acquisition types

## Slide 7: Tiled pyramidal or Mosaic Stacks

## Slide 8: Ex-vivo confocal microscopy
Freshly excised tissue
Fluorescent stain
Reflectance or Fluorescence modes

## Slide 9: Ex-vivo RCM of BCC Specimen with acridine orange stain
Reflectance
Fluorescence
Image source https://onlinelibrary.wiley.com/doi/full/10.1111/bjd.18239

## Slide 10: Progress
Major changes
  Originally 1 IOD now 3 IODs
  Additional IODs Confocal Microscopy Tiled Pyramidal Image IOD and Confocal Microscopy Multi-Frame Image IOD
  Skin Cancer Acquisition Context > Skin Imaging Acquisition Context
  Add CID Specimen stains for CM (do not use existing CID)
  Added Acquisition IE and Multi-Resolution Pyramid IE, Slide Pyramidal Tile Organisation module, Removed ICC Profile module
  Moved some content to PS3.17
  Added explanatory diagrams
  Re-used attributes (power, wavelength) from OCT
Minor changes
  Formatting and organisation
  Value representations
  Added microscope to Optical Magnification Factor