## Slide 1: Public Comment Overview: Supplement 235: HTJ2K Transfer Syntax
Bill Wallace, Radical Imaging
Chris Hafey, Amazon Web Services
DICOM WG-04 - Compression

## Slide 2: Challenges with Existing Compression
  JPEG 2000 has advanced features but has seen low adoption
      Significantly slower than other transfer syntax (at least 5x slower than JPEG-LS to decode)
      Advanced features require image to be encoded using specific parameters (e.g. scalable resolution requires RPLC progression order, certain number of decompositions)
      Very complex to implement correctly (several interoperability issues early on)
      Lack of availability of open source implementations for many years (paid commercial libraries was the only option)
      Concerns over patent conflicts (increased risk of litigation)
    JPEG Lossless and JPEG LS
      Do not support scalable resolution access
      Little to no gain from parallelization (not designed for this)

## Slide 3: HTJ2K Compression
JPEG2000 was extended in 2019 with a new block coder that improves decode and encode speed by an order of magnitude. This variant of JPEG2000 is referred to as High Throughput JPEG2000 (HTJ2K)
ISO/JPEG standard (https://jpeg.org/jpeg2000/htj2k.html)
Free of patent conflicts, royalty free
Strong Open Source support (OpenJPH, OpenJPEG, GROK, ffmpeg)
Slightly lower compression ratios than JPEG2000 (~5%)
Significantly faster at decoding than all compressed transfer syntaxes by at least 50% -> improved image display speed
Supports most of the advanced JPEG2000 features (scalable resolution access in particular)
Lower implementation complexity
Learn more: https://github.com/chafey/HTJ2KResources

## Slide 4: Resolution Scalability
128x128
(10KB)
256x256
(30KB)
512x512
(90KB)
HTJ2K Lossless CT Image - 140KB Total
Download
Viewer can dynamically improve the displayed image quality by decoding and rendering the image bitstream as it is received. This results in better user experiences, especially over lower and variable bandwidth network connections
Decode/Render
Decode/Render
Decode/Render
Download
Decode/Render
Viewer can display a 128x128 thumbnail of an image (e.g. series browser) by reading a small number of bytes (10K) of the bitstream. This results in faster initial loading, less bandwidth consumption and lower implementation complexity
Try it out: https://chafey.github.io/openjphjs/test/browser/index.html
Learn more: https://docs.google.com/document/d/1hMv75h8g5a8EvIopucdhElKdu7QGF1PgpAK4J1Ahvp4/edit?usp=sharing

## Slide 5: Changes Overview
Add lossy and lossless Transfer Syntaxes for HTJ2K
Add constrained lossless Transfer Syntax to ensure applications can leverage scalable resolution features
Add HTJ2K as a DICOMweb rendered media type for faster decoding and smaller image sizes

## Slide 6: Conclusions
HTJ2K brings significantly faster image decoding for all image types -> faster image access
The new constrained transfer syntax ensures HTJ2K images are encoded properly for scalable resolution access -> applications can confidently use this powerful feature